## Slide 1
THANK YOU TO OUR GENEROUS SPONSORS
FOR SUPPORTING THE CALTECH SPACE CHALLENGE

## Slide 2: Project Explorer
27 March 2015
Lunar – reDirected Orbiting Resource Asteroid Demonstration and Operation

## Slide 3: The Big Picture
Project Explorer brings astronauts to the lunar orbiting ARM asteroid in 2025 to characterize, extract, and utilize its resources in order to demonstrate the potential benefits for humanity and future exploration missions.

## Slide 4: Executive Summary
Two rockets: One for cargo and one for crew
The Eureka science module launches in August 2024 and heads to the asteroid
A 3-person crew launches in February/March 2025
8.5 day prograde lunar flyby trajectory to reach the asteroid
22 days of on-asteroid operations
  Characterization of the asteroid and its environment
  Resource extraction, processing, and utilization
  Public outreach
8.5 day trajectory to return to earth
Abort options drive mass and schedule design limits
Uses Orion and SLS architecture
$3.1 billion projected cost ($1.8 Billion without launch costs)

## Slide 5: Presentation Flow
Build the foundation
Make it flexible
Make it creative
Make it fun

## Slide 6: Table of Contents
Mission Context
Mission Overview
Trajectory and Launch
Science and Technology Demos
Human Factors and ECLSS
System Engineering
Public Outreach
Budget
Conclusions

## Slide 7: Introduction: Step One

## Slide 8: Introduction: Step Two
Now What?

## Slide 9: Critical Ground Rules and Assumptions
In place by 2024
Class “C” Asteroid
500 metric tons
Design for A or B
ARM Power can be used
Use SLS and Orion for Crew
Block 1, 1B Available
Block 2 Maybe Not
2+ Astronauts
TRL 8+
Standard NASA Procedures
International Cooperation
Public Outreach is Critical
Planetary Protection Mandate

## Slide 10: Mission Overview
Moon flybys
LEO
DRO
Crew Vehicle Launch
SLS Block 1 B
Cargo Mission
Falcon Heavy
Earth
Return as heroes!
Time
August 2024
February-March 2025
Moon
Low-energy Ballistic Capture
(0 m/s)
Prograde Lunar Flyby
(190 m/s)
Orbit Insertion (318 m/s)
Reentry Velocity: ~11 km/s
Crew TOF: 39 days
DRO Departure
(318 m/s)
Lunar Flyby
(190 m/s)
Scientific Exploration:
22 days
TOF: 4-6 months
Outbound TOF: 8.6 days
Inbound TOF: 8.6 days
Notes: For H Transfer of Cargos  Estimated Time: 7-8 months

## Slide 11: Trajectory Planning: The Asteroid’s Orbit
Period of DRO = 11+ days
61,500 km
Bezrouk, Collin, and Jeffrey Parker. "Long Duration Stability of Distant Retrograde Orbits." AAS (2014): n. pag. Web.
Our DRO
Notes: We computed the points of the DRO

## Slide 12: Launch strategy
Rocket | Mass to TLI (t) | Payload | Payload mass (t) | Launch date
Falcon Heavy | ≤ 18 | Eureka | 17.2 | August 2024
SLS Block 1B | ~ 47 | Orion | 36 | February 20, 2025
SLS may only be able to launch once per year; need SLS for Orion launch
Baseline: Launch 1 - Falcon Heavy, Launch 2 - Orion
SLS Block 2 can be used if available (2024?) -> Only one launch needed
2 Launches
Liftoff
T = 0 s
SRB Jettison
T + 128 s
Payload Fairing and
Launch Abort Jettison
T + 472 s
Core & Upper Stage Separation
T + 476s
Upper Stage Ignition
T + 486s
Upper Stage Separation
T + 1,821 s
SLS Launch Sequence

## Slide 13: Transit: Eureka Trajectory
Maneuvers for Outbound Trajectory | Time since launch [mo.] | Δv [m/s]
Launch “cleanup” | ~ 0 | 15
Rendezvous/Docking | 4-6 | 15
30 m/s
Low-Energy Ballistic Capture
Herman, Jonathan F.C., and Jefferey S. Parker. "Low-Energy, Low-Thrust Transfers Between Earth and Distant Retrograde Orbits about the Moon." Annual AAS Guidance & Control Conference (2015): n. pag. Web.
SEP was also considered but not selected because of additional system complexity

## Slide 14: Transit: Crew Trajectory Options
Outbound/Inbound Option | Δv [m/s] (one-way) | TOF [days]
Direct Transfer | 600 | 5.9
Prograde Powered Lunar Gravity Assist | 508 | 8.6
Retrograde Powered Lunar Gravity Assist | 299 | 13.5
Retrograde Powered Gravity Assist
Direct Transfer
Prograde Powered Lunar Gravity Assist
Landgraf M., Duering M., and Renk F. “Mission Design Aspect of European Elements in the International Space Exploration Framework”

## Slide 15: Transit: Crew Trajectory
Maneuvers for Outbound Trajectory | Time since launch [days] | Δv [m/s]
Launch “cleanup” | ~ 0 | 20
Gravity Assist | 4.6 | 190
DRO Injection | 8.6 | 318
Rendezvous/Docking | 8.9 | 15
Maneuver for Inbound Trajectory | Time since launch [days] | Δv [m/s]
DRO Departure | 30.6 | 318
Gravity Assist | 34.6 | 190
1051 m/s
Landgraf M., Duering M., and Renk F. “Mission Design Aspect of European Elements in the International Space Exploration Framework”
1338 m/s

## Slide 16: Transit: Launch Date and Time Selection
Moon orbit plane (inclination and RAAN)
Cargo Launch
08/2024
Crew Launch
03/2025
http://qrznow.com/wp-content/uploads/2014/09/Prediction_Solar_Cycle_-25_HFLINK-190x122.png
Preferred Launch Dates
RAAN: one launch opportunity per day
Optimal Launch Opportunity: Arriving at DRO at the lunar perigee within the above windows. (reduced time of flight and ΔV)

## Slide 17: Science and Tech Demonstration Objectives
 | Decadal Survey/Stratgic Knowledge Gap | Objectives
S1 | Understanding Solar System Beginnings | Quantify composition, characterize surface processes, probe internal structure, characterize water phases
S2 | Revealing Planetary Processes through Time | 
S3 | Searching for the Requirements for Life | Detect and identify organic compounds
T1 | In-situ Excavation of Small Body Material | Excavate enough rocks for 5 kg of water
T2 | Extraction of Resources from Excavated Material | Extract water, separate oxides
T3 | Demonstrate Utilization of Extracted Resources | Steam rocket, H/O, sintering, radiation+thermal shielding experiment, experimental garden

## Slide 18: Operations Plan – Days 1-11
1
2
3
11
10
9
4
6
5
8
7
science drilling campaign
pyrolysis
EVA 1
set up science
drill
collect surface
samples
install pyrolysis
chamber
EVA 2
-operate
plasma drill
-collect
science core
-load pyrolysis
chamber
adaptation
begin breathing protocol
begin breathing protocol
+ surface sample analysis
testing surface samples
surface samples analysis
surface samples analysis
samples analysis
samples analysis
radiation shielding exp. prep.

## Slide 19: Operations Plan – Days 12-22
More science on Earth:
dating, isotopes, space weathering,
oxides, silicates, etc.
12
13
14
22
21
20
15
17
16
19
18
pyrolysis
EVA 3
-collect
pyrolysis
end-product
-sinter
-shielding
experiment
-load steam
rocket
-deploy
SPHEREs
-outreach
packing and disposal
shielding experiments campaign
experimental garden
radiation shielding exp. testing
samples analysis
samples analysis
samples analysis
samples analysis
+ astronaut sorbet
samples analysis
oxides separation
steam rocket
+ electrolysis (H/O)
water purification
+ start experimental garden

## Slide 20: Science: Primary Instruments
Chemistry
Alpha Particle X-Ray
Mineralogy
Active hyperspectral VISIR spectrometer
X-Ray Diffractometer
Sampling
Coring Drill
Chisel-in-a-Cup
Imaging
High-Res Camera
Microscopic Imager
Structure
Density Probe
Neutron Probe
Gamma Ray Probe
Thermocouples
Organics
Gas Chromatography -Mass Spectrometer
Radiation
Radiation Detectors

## Slide 21: ISRU: Extracting Volatiles from Ore
Pressure valve opens to condenser at 1 atmosphere
  Initially water vapor and then liquid water in container
Heating via resistance heaters and propeller for circulation
Minimum 5 kg water extracted
Centrifuge then separates volatiles
Pyrolysis Chamber (400-600°C)
Condenser 10°C
MLI
Wire mesh ore carrier
Water chamber for initial advection gas
Max ore capacity = 250 kg
0.5 m internal diameter
Circulation Propeller

## Slide 22: Tech Demos: Steam Rocket, Radiation Shielding
Test 15 kg steam rocket
  Concentrated sunlight vaporizes asteroid water  thrust
  Low ISP (~40 sec)
Good for on/near asteroid operations
  Rugged, simple engine
  Fuel easy to store as ice
Steam Rocket (Nakamura)

## Slide 23: Tech Demo: Semi-Autonomous Robotic Swarm
Derived from the MIT SPHERES-project
Allow for remote and local control
Leave behind as “inhabitants”
Augment situational awareness
Increase outreach capabilities

## Slide 24: ISRU: Solar Powered Sintering

## Slide 25: ISRU: Plant Experiment

## Slide 26: Adding Value: Use ARM’s 50 kW Power and Eureka
50 Kilowatt Deep Space Network
Wireless Power Demo
Resource Depot
Moon/Mars Abort Station

## Slide 27: Physiological Deconditioning & Countermeasures
-Typical countermeasures for in-flight, pre-landing, post landing
-Resistive Exercise Device: Rotary MR Damper
-current TRL level of 3, expected TRL level of 7 at TOF
-specifically developed for compact volumes
-Radiation Protection: water walls in Eureka, X-ray monitoring using GOES
-no risk of GCR / risk of SPE
-changes in HR, cephalic fluid shift, bone mass density loss, cardiovascular changes, muscle atrophy, radiation protection
Selection
- 2 x scientists, 1 x engineer
- odd numbered crew to avoid decisional splits
- people of task-focused styles perform better: aptitude, personality, attitudes, experiences, communication skills
-Psychological training
-Survival training
-Group building activities
-Training together
Crew Size, Selection, Training
Training
Notes: bone mass loss rates, resorption vs formation

## Slide 28: ECLSS: Understanding Orion

## Slide 29: ECLSS: Building an Independent System

## Slide 30: ECLSS: Eureka Environmental Control & Life Support Systems
Water Recovery & Purification
-Vapor Phase Catalytic Ammonia Removal (VPCAR) System
-Trades included ISS Water Recovery System & Forward Osmosis Bag
Atmospheric Monitoring & Regulation
CO2 Reduction: Sabatier (chosen over Bosch and LiOH)
Non-regenerable O2 generation: O2 tanks
Sensor suite for monitoring
TCCS: charcoal sorbent bed to catalytic oxidizer
Fire detection & suppression: JPL E-Nose
Demonstration for future ECLSS Reservoirs
Oxygen Generation with H2 byproduct as Rocket Fuel Source
Solid Polymer Electrolyte Water Electrolysis
-scaled down electrolysis
-typical of ISS Oxygen Gen
Assembly
-demo for future O2 and H2
reserves

## Slide 31: ECLSS: IVA Space Suit Selection
ACES (Advanced Crew Escape Suit)
MACES (Modified ACES)
9 | Current TRL | 6
9 | 2025 TRL | 8
41.7 | Total Mass (kg) | 16
Shuttle | Vehicle Design Fit | Orion
Vehicle Provided - Open-loop | Primary Life Support | Vehicle Provided - Closed-loop
No | EVA Capability | Yes
$180,000 | Cost | Unknown (Est. $360,000)

## Slide 32: ECLSS: EVA Space Suit Selection
EMU (Extravehicular
Mobility Unit)
- TRL Level 9: Flight Proven
- Suit Mass: 55.3 kg
- Life Support: PLSS
- Nominal EVA Time: 8 hours
- EVA Mobility: Moderate
- TRL Level 7: Demonstrated in
operational environment
- Suit Mass: 36 kg
- Life Support: PLSS 3.0
- Nominal EVA Time: 10 hours
- Mobility: Low
MACES (Modified ACES) Suit
Z-3 (Z-Series) Exploration Suit
- TRL Level 6: Demonstrated
- Expected TRL Level 9 by 2022
- Suit Mass: 65 kg
- Life Support: PLSS 3.0
- Nominal EVA Time: 10 hours
- Mobility: High
- Future Mars Exploration Suit

## Slide 33: Systems Engineering: Requirements
# | Functional Objective
1 | Safely bring and return humans to the ARM asteroid
2 | Characterize the asteroid and its environment
3 | Demonstrate the feasibility of in situ resource use for long term missions
4 | Involve and inspire the public
All of the requirements are driven by four functional objectives:
# | Functional Objective
1 | Safely bring and return humans to the ARM asteroid
1.1 | Protect the crew from the aerospace environment.
1.2 | Provide sufficient propulsion capability to meet the science and demonstration objectives.
1.3 | Design abort options to minimize crew return delays.
These functional objectives have children requirements. For example:

## Slide 34: Systems Engineering
Payload Budget - Orion
System | Mass [t] | Volume[m3]
Orion | 10.2 | 
Fairing, LAS, Docking | 9.5 | 
Service Module | 16.0 | 
Human Factors | 0.65 | 3
Astronauts | 0.29 | 6
Total | 0.94 | 9
Margin | 0.2 | 0.2
Total + Margin | 36.82 | 10
Payload Budget - Eureka
System | Mass [t] | Volume[m3] | Power avg. [kW]
Habitat | 3.3 |  | 
Science | 0.98 | 13.4 | 
ECLSS | 8.75 | 3.6 | 2.3
Workspace |  | 10.8 | 
EPS | 0.23 |  | 3.0
TCS | 0.04 | 0.1 | 1.5
GNC | 0.93 |  | 257.4
COM | 0.08 |  | 72.0
OBDH | 0.01 |  | 20.2
Module Structure | 0.5 |  | 
Total | 14.35 | 28.0 | 2.6
Margin | 0.2 | 0.2 | 0.2
Total + Margin | 17.22 | 33.6 | 3.2
 | Mass [t] | Power [kW]
Total | 51.0 | 47.2
Margin | 0.2 | 0.2
Total + Margin | 54.1 | 56.7
Total

## Slide 35: EPS
Power Budget
Primary and secondary batteries in Eureka
Solar array sizing includes required battery charge power
Peaks covered by batteries
Chart: Days after Eureka launch
| 0 | 180 | 180 | 202 | 218.6 | 218.6 | 240.6 | 240.6 | 249.2
Eureka Required | 0.32831 | 0.32831 | 3.1888 | 3.1888 | 3.1888 | 3.1888 | 3.1888 | 0.32831 | 0.32831
Orion Total Req | 11.1 | 11.1 | 55.1748 | 55.1748 | 11.1 | 11.1
Eureka Available | 4.7831 | 4.7831 | 54.7831 | 54.7831 | 54.7831 | 65.8831 | 65.8831 | 54.7831 | 54.7831
Orion Total Avail | 11.1 | 11.1 | 65.8831 | 65.8831 | 11.1 | 11.1
On Site Peak | 3.5098 | 3.5098 | 6.3703 | 6.3703 | 6.3703 | 68.9153 | 68.9153 | 6.3703 | 6.3703

## Slide 36: Risk management
Risks related to all subsystems are rated according to the NASA risk management standard.
Mitigation strategies are implemented according to the severity
Almost all critical risks reduced to LOM
10: Partial failure of critical system shortly after TLI  Trajectories and maneuvers devised to bring crew back to earth
Consequence Index/ Probability Index | 1 | 2 | 3 | 4 | 5
5 | 23 |  | 8 |  | 
4 |  |  | 30 | 21/22 | 
3 | 31 | 12 | 11/16/17/20/24 |  | 10
2 | 3/15 | 18 | 2/25/26/27 | 5/6/7/13 | 14
1 | 4 | 1 |  | 29 | 9/19/28

## Slide 37: Science Habitat - Eureka
Inflatable
Based on TransHab studies and Bigelow
Mass interpolated from available data
Augments Orion capabilities
Length: 7m
Diameter: 7.5m
SPE Shelter Area
48m3 in center axis
for instruments/equipment
40m3 additional space
0.5m thick inflatable skin
Eureka Service Module
Docking adapters

## Slide 38: Launch configuration
SLS Block 1B
Falcon Heavy
Secondary payload
 Outreach
Deflated Eureka

## Slide 39: Public Outreach: Tangible Experiences
Space selfies
Arm-Chair Astronauts
Astronaut Sorbet from Processed Water
CubeSats Released at Moon (After Mission)

## Slide 40: Public Outreach: Social Media in Action
Discussion on the International Space University Page
1,500+ People Reached
Picked up by the Space Generation Advisory Council
Created a Facebook Page

## Slide 41: Programmatic Considerations: Budget
Rough estimates of the mission cost are based on the Space Mission Analysis and Design handbook
Launch costs are best guess and do not include development costs
Development of common technologies not included: Orion and SLS program, Orion Service Module (MPCV-ESM), Space suit, annual cost of launch and NASA facilities, Bigelow space module
Item | ROM cost (M$)
2.0 Launch Vehicle | 
2.1 First launch (Falcon Heavy) | 270
2.2 Second launch incl. Orion capsule and service module (SLS block 1B) | 2,000
Total | 2,270 M$
Launch costs

## Slide 42: Programmatic Considerations: Budget
Rough estimates of the mission cost are based on the Space Mission Analysis and Design handbook
Launch costs are best guess and do not include development costs
Development of common technologies not included: Orion and SLS program, Orion Service Module (MPCV-ESM), Space suit, annual cost of launch and NASA facilities, Bigelow Module
Vehicle and operation costs
Item | ROM cost (M$)
1 Science vehicle assembly | 
1.1. Inflatable structure | 150
1.2. Custom service module | 250
1.3. Science and tech demo | 700
3.0 Ground Command & Control | 50
4.0 Program level | 220
7.0. Operations | 130
Total (with 20% margin) | 1,800 M$

## Slide 43: Conclusions: Mission Overview
x3
+
39 Days

## Slide 44: Conclusions: Measure, Treasure, and Pleasure
Science
Outreach
Utilization

## Slide 45: Conclusions: We Should be Having Fun Too!

## Slide 46: But Seriously…
Moore-Hufstedler Fund
mhf.Caltech.edu
And to the Caltech Space Challenge mentors, speakers, and organizers!

## Slide 48: Trajectory Planning: Direct Transfer Abort Option
TOF = 6 days
Williams & Condon, “Contingency Trajectory Planning for the Asteroid Redirect Crewed Mission,” Paper AIAA 2014-1697

## Slide 49: Communications, Command and Data Handling
Two links :
Telemetry link
Crew voice communiction link
High system complexity : Science Data, HD cameras, housekeeping data
C&DH system : 10 kg, 15 dm3 and consume 25 W (‘SMAD’, Wertz)
Time of lunar blackout time ~ 2 h (no operations that require communications fidelity.
ARCHITECTURE
Link budget assumptions:
Data rate: 12 Mbps
X-band frequencies : ~8 GHz Total losses : 12 dB Thermal noise : neglected Ground station : 15 m dish, 200 W
Various losses outside line losses: 12 dB
S/C dish of 10 cm diameter and a power of 20 W
Link closes with margins of 20 dB on the up- and 11 dB downlink.

## Slide 50: We Had Fun (Ridiculous) Ideas Too
Break up the asteroid and send it to earth to create a spectacular meteor shower.
Expect a huge spike in weddings and wedding proposals on the day of the event.

## Slide 51: Back-up Slides

## Slide 52: “Hot” Issues
Working hard across disciplines to get everything in one launch. Going to be close.
Difficult to find mass, power, volume, cost, etc… information on existing science instruments.
In situ resource processing doesn’t have much real-world experiments to study.
Looking to push the envelope on creativity. Would like to get your feedback on some concepts. (See back up slides)

## Slide 53
Science Missions
Use the resources for future moon and mars missions.
Use a mirror to focus the sun to sinter material.
Build a symbiotic greenhouse where microbes create the resources needed to fuel the plants.
Leave an autonomous station that continues to research and process the asteroid
Use the asteroid as a platform for deep space communications. It could feature both laser powered as well as traditional EM technology. It may be even more valuable as a telecommunications platform if it's in a polar orbit around the moon.
Install telescopes that will benefit from using the asteroid as an effective sun and earth shield.
Use it as an emergency station for moon travelers.
Use the gases and water collected from the asteroid to power a small rocket that navigates around, or possibly to, the moon. It would be more of a steam rocket then a high Isp rocket.
The asteroid's relatively wide orbit around the moon may make it a good platform for radio wavelength observations. The asteroid would also help block polluting signals from the earth.
Use the asteroid to demonstrate micro-gravity refueling.
Use the asteroid for radiation protection, either by boring into it or breaking it into smaller pieces that are installed around a vehicle.

## Slide 54
Science Missions
Use bacteria or microbes to digest the asteroid over time. A bag or balloon around the asteroid collects the gases for analysis and use later.
Use the mass of the asteroid to help demonstrate artificial gravity methods.
Use the asteroid as a platform for the Mars Cycler concept.
Beam the 50 kWatts from the ARM to earth to study space-based energy sources. Alternatively, beam the power to a relatively nearby test unit.
Cut the asteroid in half with a laser. Science!
Lunar science base. Green house on moon. Futuristic approach. Telerobot control
Crash the asteroid on the moon, Mars, Venus, etc... to create a plume that can be studied.
Use the minerals from the asteroid to create a solar panel.
Use the moon's tidal forces to break apart the asteroid.
Break the asteroid into pieces, then embed life in the asteroid and send them outside the solar system.
Demonstrate the ability to precisely target and collide with another asteroid.
Use a laser to shape the asteroid, get it to start spinning, and become a reaction wheel.
Testing asteroid deflection technologies for earth protection.
Break up the asteroid and send it to earth to create a spectacular meteor shower. Expect a big spike in wedding proposals.

## Slide 55: Launch 1: Falcon Heavy Launch
Liftoff
T = 0 s
Boosters Jettison
T + 165 s
Core & Upper
Stage Separation
T + 210 s
Upper Stage Ignition
T + 220 s
Payload Fairing Jettison
T + 225 s
Upper Stage
Separation
T + 600 s
Launch Date:
January 4th, 2024
Payload: Science Module
Rocket | Mass to TLI (kg)
Delta IV Heavy | 11,350
Falcon Heavy | 16,280
SLS Block 1 | 21,660
Must deliver science module mass of 12,000 kg to Trans-Lunar Injection (TLI)
Only Falcon Heavy and Space Launch System (SLS) are sufficient
SLS may only be able to launch once per year; need SLS for Orion launch
Thus, Falcon Heavy will be used to launch science module

## Slide 56: Launch 2: Space Launch System 1B Launch
Liftoff
T = 0 s
SRB Jettison
T + 128 s
Payload Fairing and
Launch Abort Jettison
T + 472 s
Core & Upper Stage Separation
T + 476s
Upper Stage Ignition
T + 486s
Upper Stage Separation
T + 1,821 s
SLS Variant | Total Delivered Mass to TLI (kg) | Supplementary Mass (kg)
Block 1 | 28,990 | not available
Block 1B | 46,960 | 11,580
Block 2 | 52,410 | 17,030
Supplementary mass is total mass subtracted by Orion launch mass of 35,385 kg
Space Launch System Block 1B (available 2021) and Block 2 (available 2024?) are sufficient
SLS Block 1B will be used; SLS Block 2 can be used if available -> Only one launch needed
Stage breakdown by thrust, specific impulse, and mass available in backup slides
Launch Date:
January 4th, 2025
Payload: Orion

## Slide 57: Launch Backup
Stage | Variant | Rocket Engine | Thrust (kN)* | Isp (s)^ | Burn Time (s) | Dry Mass (t)* | Propellant Mass (t)*
0 | 1/1B | 2x Modified SS SRBs | 28024 | 252.2 | 128.4 | 104 0. | 631.5
 | 2 | 2x New Composite ATK Boosters | 40031 | 272.5 | 110 | 84 | 790
1 | 1/1B/2 | 4x RS-25D/E | 8277 | 409.1 | 476 | 102 | 979.5
2 | 1 | 1x RL-10-B2 | 110 | 461.5 | 1118 | 3.8 | 26.9
 | 1B/2 | 4x RL-10-C1 | 425 | 448.5 | 1335 | 15 | 129

## Slide 58
2019
2025
2028-2029
Delta IV Heavy
SLS Block 1B
ARM Option A
Lunar DRO
Configuration Change
Return
Team Explorer

## Slide 59: Mission Overview
LEO
DRO
Crew Vehicle Launch
SLS Block 1b
Earth
Return as National Heroes
Time
Time
Timeline not to scale
March-April 2025
Moon
Prograde Lunar Flyby
(190 m/s)
Orbit Insertion (318 m/s)
Reentry Velocity: ~11 km/s
Stay at asteroid: 11 days
Crew TOF: 28 days
DRO Departure
(318 m/s)
Lunar Flyby
(190 m/s)
TLI
(3.1 km/s)

## Slide 60: Trajectory Planning: Reentry Velocity
v = ~11 km/s

## Slide 61: Tech Demo: Plasma Drill and Radiation Protection

## Slide 62: ARC (Asteroid Regolith Crusher)
Cone crusher
Used on earth
Development needed for deep space implementation
Needs self cleaning environment
Rotating cone
Drive
Pressurized gaz container
Spring loaded feeder
Crushing surfaces
Reciever (vacuum cleaner bag)

## Slide 63: ISRU: Microbe Powered Greenhouse
+
=

## Slide 64
30 kW microwave emitter
  ~65-78 % efficiency – difficult to remove waste heat
  Safety concerns with crew nearby
Solar thermal – parabolic mirrors
  Long set up time, limited EVAs
  Area >20m2
  Pyrolysis chamber must be uninsulated
  Astronauts could pass in front of beam
Alternative Pyrolysis Heating Methods (Backup)

## Slide 65: Engineering
Engineering of the vehicles, tools, and instruments primarily relies on the subcontractors.
The program levies requirements based on mission level analysis and assigns factors of safety they must work to.
The general concept is to define what they must not do and not how they must do it.

## Slide 66: Programmatic Considerations (Backup)
Cost
Item | ROM cost (M$) | Comment | Num FTE over 10 years
1.0 Space Vehicle |  |  | 
1.1. Orion capsule with service module | 1000 | From web | 
1.2. Service transfer vehicle | 0 | Assumes European contribution | 
1.3. Science payload |  |  | 
1.3.1. Laboratory structure | 148 | USCM8: ~(23 k$/kg * 4000kg * 150%) | 
1.3.2. Laboratory thermal control | 6 | USCM8: ~(23 k$/kg * 136kg * 150%) | 
1.3.3. Science instruments | 500 | 20 instruments @ 20 M$ + 25% | 
2.0 Launch Vehicle (launch cost) | 1000 | From web | 
3.0 Ground Command & Control | 5 | 3% of laboratory cost | 
4.0 Program level |  |  | 
4.1. System engineering | 31 | 20% of laboratory cost (not instruments) | 16
4.2. Program management | 24 | 15% of laboratory cost | 12
4.3. System integration and test | 24 | 15% of laboratory cost | 12
4.3. Product assurance | 5 | 3% of laboratory cost | 3
4.5. Other | 0 |  | 
5.0 Flight Support Operations | 0 |  | 
6.0 Aerospace Ground equipment | 0 |  | 
7.0. Operations |  |  | 
7.1. PMSE | 24 | 15% of laboratory cost | 
7.2. Space segment maintenance | 0 |  | 
7.3. Ground segment | 9 | 30 engineers + 10 tech, for 2 months | 

## Slide 67: Team Members
First Name | Last Name | Focus Areas
Bill | Tandy | Proposal Manager
Chris | Wynard | 
Dan | Fries | Systems Engineering
Davide | Conte | 
Henna |  | 
Koki | Ho | 
Lee |  | 
Max |  | 
Marilena |  | 
Mat |  | 
Max |  | 
Priyanka |  | 
Rahul |  | 
Simon | Dandavino | 
Takeshi | Gagliardi | 
Thierry | de Roche | Extraction
Valentina | Boccia | Science

## Slide 68: Launch
Launch concept trade-off
A | Orion + Service Module in SLS Block 1B and Habitat in Block 1B |  |  | 
B | Orion + Service Module in Block 1B and Habitat + Heavy Lift + Upper Stage in Payload for ballistic TLI |  |  | 
C | Orion + Service Module in Block 1B and Inflatable Habitat + Heavy Lift for ballistic TLI |  |  | 
D | Orion + Service Module in Block 1B and Habitat + Heavy Lift + SEP to lunar DRO |  |  | 
E | Orion + Service Module in Block 1B and inflatable Habitat + Heavy Lift + SEP to lunar DRO |  |  | 
Chart: Risk
| 10
A | 90
B | 40
C | 50
D | 60
E | 80
Option B - large, cryogenic upper stage, modified payload fairing
Option D - more costly due to customized habitat, additional ARM derived SEP module.
Can-designs have large heritage, ARM is intentionally developed modularly to reuse
Option C - good compromise between risk and cost, chance to develop inflatables further, key technology for future missions. Enough payload volume and mass, including sufficient margins.

## Slide 69: Risk Management
Critical Risks
8: Translunar injection maneuver is not successful  If the upper stage delivers only a delta-v of 2.92 km/s or lower, the mission cannot be completed (still working on mitigation!)
21: Eclipse by moon/earth
MLI in skin of Eureka to ensure thermal inertia. Include heating device.
22: Eclipse by asteroid
Dock in such a way that spacecraft is not eclipsed. Include heating device.

## Slide 70: Launch Trade Example
A | Orion + Service Module in SLS Block 1B and Habitat in Block 1B | 
B | Orion + Service Module in Block 1B and Habitat + Heavy Lift + Upper Stage in Payload for ballistic TLI | 
C | Orion + Service Module in Block 1B and Inflatable Habitat + Heavy Lift for ballistic TLI | 
D | Orion + Service Module in Block 1B and Habitat + Heavy Lift + SEP to lunar DRO | 
E | Orion + Service Module in Block 1B and inflatable Habitat + Heavy Lift + SEP to lunar DRO | 
Chart: Risk
| 10
A | 90
B | 40
C | 50
D | 60
E | 80
Option B - large, cryogenic upper stage, modified payload fairing
Option D - more costly due to customized habitat, additional ARM derived SEP module.
Can-designs have large heritage, ARM is intentionally developed modularly to reuse
Option C - good compromise between risk and cost, chance to develop inflatables further, as a key technology for future missions. Enough payload volume and mass, including sufficient margins.

## Slide 71: Eureka
Habitat trade-off
Science equipment and experiments require considerable amount of space
Improved radiation shielding allows for extended stay
Inflatables as key technology for future manned exploration and utilization missions
More usable payload per launch
Inflatable heritage does exist
 | “Can” design | Inflatable
Living/Working Space | + | +++
Heritage | +++ | +
Radiation Shielding | ++ | +++
Mission Duration | + | ++
Tech. advancement | + | ++
Mass | + | ++
Cost | ++ | +
Total | 11 | 14

## Slide 72: Programmatic Considerations (Backup)
Cost
Item | ROM cost (M$) | Comment | Num FTE over 10 years
1.0 Space Vehicle |  |  | 
1.1. Orion capsule with service module | 1000 | From web | 
1.2. Service transfer vehicle | 0 | Assumes European contribution | 
1.3. Science payload |  |  | 
1.3.1. Laboratory structure | 148 | USCM8: ~(23 k$/kg * 4000kg * 150%) | 
1.3.2. Laboratory thermal control | 6 | USCM8: ~(23 k$/kg * 136kg * 150%) | 
1.3.3. Science instruments | 500 | 20 instruments @ 20 M$ + 25% | 
2.0 Launch Vehicle (launch cost) | 1000 | From web | 
3.0 Ground Command & Control | 5 | 3% of laboratory cost | 
4.0 Program level |  |  | 
4.1. System engineering | 31 | 20% of laboratory cost (not instruments) | 16
4.2. Program management | 24 | 15% of laboratory cost | 12
4.3. System integration and test | 24 | 15% of laboratory cost | 12
4.3. Product assurance | 5 | 3% of laboratory cost | 3
4.5. Other | 0 |  | 
5.0 Flight Support Operations | 0 |  | 
6.0 Aerospace Ground equipment | 0 |  | 
7.0. Operations |  |  | 
7.1. PMSE | 24 | 15% of laboratory cost | 
7.2. Space segment maintenance | 0 |  | 
7.3. Ground segment | 9 | 30 engineers + 10 tech, for 2 months | 

## Slide 73: Public Outreach: Tangible Experiences
Art Using Returned Asteroid Material
CubeSats Released at Moon (After Mission)
Name the Asteroid Leave Disc of Names
Astronaut Sorbet from Processed Water

## Slide 74: References
TBD

## Slide 75: Programmatic Considerations