## Slide 1: Trajectory Design Techniques for Human Missions to Mars Damon Landau and Nathan Strange Jet Propulsion Laboratory, California Institute of Technology
Cislunar Missions
Mars Moons
Asteroid Missions
Mars Surface
Earth
Moon
Moon’s Orbit
Low-Perigee HEO
High-Perigee HEO
Phobos capture
Deimos escape
© 2013 California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: Delta-V for Deep Space Missions
This plot shows the ΔV required to allow at least one mission every Earth-Mars synodic period (2.14 years)
Lunar orbit
Cislunar missions
10 m NEAs
30 m NEAs
300 m NEAs
60 m NEAs
100 m NEAs
600 m NEAs
diameter estimates assume 15% albedo
1 km NEAs
Phobos / Deimos
Phobos / Deimos
Total ΔV [km/s]
Crew Flight Time [days]

## Slide 3: Mean-old Mr. Rocket Equation
Chart: Delta-V [km/s]
| 3 | 3.2 | 3.4 | 3.6 | 3.8000000000000007 | 4.0000000000000009 | 4.2000000000000011 | 4.4000000000000012 | 4.5999999999999996 | 4.8000000000000016 | 5.0000000000000018 | 5.200000000000002 | 5.4000000000000021 | 5.6 | 5.8000000000000016 | 6.0000000000000027 | 6.2000000000000028 | 6.400000000000003 | 6.6000000000000005 | 6.8000000000000016 | 7.0000000000000044 | 7.2000000000000037 | 7.4000000000000039 | 7.6000000000000041 | 7.8000000000000043 | 8.0000000000000036 | 8.2000000000000011 | 8.4000000000000021 | 8.6000000000000014 | 8.8000000000000007 | 9 | 9.2000000000000011 | 9.4000000000000021 | 9.6 | 9.8000000000000007 | 10 | 10.200000000000001 | 10.4 | 10.6 | 10.8 | 11 | 11.2 | 11.4 | 11.6 | 11.8 | 12
Cryogens | 0.50648 | 0.48402 | 0.46256 | 0.44205 | 0.42245 | 0.40372 | 0.38582 | 0.36871 | 0.35237 | 0.33674 | 0.32181 | 0.30754 | 0.29391 | 0.28088 | 0.26842 | 0.25652 | 0.24515 | 0.23428 | 0.22389 | 0.21396 | 0.20448 | 0.19541 | 0.18675 | 0.17847 | 0.17055 | 0.16299 | 0.15576 | 0.14886 | 0.14226 | 0.13595 | 0.12992 | 0.12416 | 0.11866 | 0.1134 | 0.10837 | 0.10356 | 0.098971 | 0.094583 | 0.090389 | 0.086382 | 0.082552 | 0.078891 | 0.075394 | 0.072051 | 0.068856 | 0.065803
Storable | 0.38988 | 0.36615 | 0.34387 | 0.32294 | 0.30328 | 0.28482 | 0.26749 | 0.25121 | 0.23592 | 0.22156 | 0.20807 | 0.19541 | 0.18352 | 0.17235 | 0.16186 | 0.15201 | 0.14276 | 0.13407 | 0.12591 | 0.11824 | 0.11105 | 0.10429 | 0.097941 | 0.09198 | 0.086382 | 0.081124 | 0.076187 | 0.07155 | 0.067195 | 0.063105 | 0.059264 | 0.055657 | 0.05227 | 0.049089 | 0.046101 | 0.043295 | 0.04066 | 0.038185 | 0.035861 | 0.033679 | 0.031629 | 0.029704 | 0.027896 | 0.026198 | 0.024604 | 0.023106
Storable (325 sec)
For lunar mission (DV ~4.5 m/s), 50 metric ton
vehicle requires a 130 t launcher
For a six-month mission to a 10 m NEA (DV ~6.5 m/s),
a 50 metric ton vehicle requires a 220 t launcher

## Slide 4: The Electric Path
Chart: Delta-V [km/s]
| 3 | 3.2 | 3.4 | 3.6 | 3.8000000000000007 | 4.0000000000000009 | 4.2000000000000011 | 4.4000000000000012 | 4.5999999999999996 | 4.8000000000000016 | 5.0000000000000018 | 5.200000000000002 | 5.4000000000000021 | 5.6 | 5.8000000000000016 | 6.0000000000000027 | 6.2000000000000028 | 6.400000000000003 | 6.6 | 6.8000000000000016 | 7.0000000000000044 | 7.2000000000000037 | 7.4000000000000039 | 7.6000000000000041 | 7.8000000000000043 | 8.0000000000000036 | 8.2000000000000011 | 8.4000000000000021 | 8.6000000000000014 | 8.8000000000000007 | 9 | 9.2000000000000011 | 9.4000000000000021 | 9.6 | 9.8000000000000007 | 10 | 10.200000000000001 | 10.4 | 10.6 | 10.8 | 11 | 11.2 | 11.4 | 11.6 | 11.8 | 12
Cryogens | 0.50648 | 0.48402 | 0.46256 | 0.44205 | 0.42245 | 0.40372 | 0.38582 | 0.36871 | 0.35237 | 0.33674 | 0.32181 | 0.30754 | 0.29391 | 0.28088 | 0.26842 | 0.25652 | 0.24515 | 0.23428 | 0.22389 | 0.21396 | 0.20448 | 0.19541 | 0.18675 | 0.17847 | 0.17055 | 0.16299 | 0.15576 | 0.14886 | 0.14226 | 0.13595 | 0.12992 | 0.12416 | 0.11866 | 0.1134 | 0.10837 | 0.10356 | 0.098971 | 0.094583 | 0.090389 | 0.086382 | 0.082552 | 0.078891 | 0.075394 | 0.072051 | 0.068856 | 0.065803
Storable | 0.38988 | 0.36615 | 0.34387 | 0.32294 | 0.30328 | 0.28482 | 0.26749 | 0.25121 | 0.23592 | 0.22156 | 0.20807 | 0.19541 | 0.18352 | 0.17235 | 0.16186 | 0.15201 | 0.14276 | 0.13407 | 0.12591 | 0.11824 | 0.11105 | 0.10429 | 0.097941 | 0.09198 | 0.086382 | 0.081124 | 0.076187 | 0.07155 | 0.067195 | 0.063105 | 0.059264 | 0.055657 | 0.05227 | 0.049089 | 0.046101 | 0.043295 | 0.04066 | 0.038185 | 0.035861 | 0.033679 | 0.031629 | 0.029704 | 0.027896 | 0.026198 | 0.024604 | 0.023106
Hall Thrusters | 0.85808 | 0.84937 | 0.84074 | 0.83221 | 0.82376 | 0.8154 | 0.80712 | 0.79892 | 0.79081 | 0.78278 | 0.77484 | 0.76697 | 0.75918 | 0.75148 | 0.74385 | 0.7363 | 0.72882 | 0.72142 | 0.7141 | 0.70685 | 0.69967 | 0.69257 | 0.68554 | 0.67858 | 0.67169 | 0.66487 | 0.65812 | 0.65144 | 0.64483 | 0.63828 | 0.6318 | 0.62539 | 0.61904 | 0.61275 | 0.60653 | 0.60037 | 0.59428 | 0.58824 | 0.58227 | 0.57636 | 0.57051 | 0.56472 | 0.55898 | 0.55331 | 0.54769 | 0.54213
Hall Thruster (2000 sec)
Storable (325 sec)

## Slide 5: Indirect Escape from Elliptical HEO
Payload Mass Fraction to HEO
3.4 km/s
0.57 km/s
Basic Strategy:
1. Use high Isp propulsion for the majority of the ΔV to get to Mars and the majority of the mass sent to Mars
2. Use high thrust propulsion for the crew

## Slide 6: Benefits of HEO Staging Node
This plot shows the ΔV required to allow at least one mission every Earth-Mars synodic period (2.14 years)
Lunar orbit
Cislunar missions
10 m NEAs
30 m NEAs
300 m NEAs
60 m NEAs
100 m NEAs
600 m NEAs
diameter estimates assume 15% albedo
1 km NEAs
Phobos / Deimos
Phobos / Deimos
Total ΔV [km/s]
Crew Flight Time [days]
HEO staging with indirect escape can lower effective mission ΔV by
~3 km/s
Target Accessibility (CP-Crew)
HEO staging with indirect escape lowers the effective mission ΔV by roughly 3 km/s
180-day missions to 10-60 m asteroids are then available every ~2 years with an effective ΔV comparable to lunar missions
With 1-year missions, the DSV could get to 100 m objects with similar effective ΔV to lunar missions
Progressively larger objects are accessible as flight time and ΔV capability approach the levels needed for Phobos / Deimos and Mars surface missions

## Slide 7: SEP Spiral
Spiral Cheatsheet for mass and time :
SEP inert mass
30 kg/kW array
15% Xe
Array to Jet efficiency
50% @ 1600 s
60% @ 2500 s
68% @ 6000 s
add margin (~10%) for radiation and shadowing

## Slide 8: Cargo pre-placement at Deimos
Earth
Deimos
The SEPC can get 54% of the IMLEO to Deimos
Cargo:
2 SEV
2 SCPS
4-year
SEP trajectory
From LEO
Single 130 t Launcher

## Slide 9: Earth Departure Strategies
Human missions to Mars require several vehicle elements with multiple launches
Elements could be aggregated at Earth-Moon L2, high-lunar orbit, high-Earth orbit, or low-Earth orbit
High level comparison of overall DV, departure windows, backup opportunities, and contingency options
  Feeds into assessments of vehicle sizing, cost, and risk

## Slide 10: Example Outbound Transfers
2033
High declination, lower C3
2035
Low declination, higher C3
180-d Earth-Mars transfers

## Slide 11: Earth Departure Asymptote

## Slide 12: Earth-Moon Lagrange Points
Moon-Fixed Rotating Perspective
Inertial Perspective
Moon’s orbit
L2 orbit
to Earth
to Earth
view from Earth

## Slide 13: Departures from L2

## Slide 14: L2 Departure Dates Free Choice Once in L2
2033
2035
Backup departure declinations are closer to lunar plane & require less DV
Backup departures require significant plane change and increase DV
Departures from L2 span approximately three days
and have an opportunity to retry Trans-Mars Injection
3-day departure window

## Slide 15: High Lunar Orbit
TMI backup opportunities occur on subsequent perigee passages
2.5-day departure window
2033
2035
Departure characteristics from high-lunar orbit are similar to L2
Low perilune and long period (100 km x 2 days) with stable orientation

## Slide 16: High Earth Orbits
Lunar gravity assists change inclination and raise perigee ~0 m/s
Lunar gravity assist
High perigee parking HEO
Apogee maneuver rotates to departure plane. ~150 m/s
Low perigee, 28.5 degree rendezvous HEO
to Mars
(large declination)
TMI ~600 m/s
High inclination departure orbit
Lunar gravity assists and maneuvers near apogee shape HEO for efficient departures

## Slide 17: 10-day HEO, 28.5 deg inclination
2033 Opportunity
Optimal free inc. (no backups)
Optimal 28.5 deg inc. (no backups)
Optimal
3-departure
orbit
Optimal
1-departure orbit
Optimal 3-departure orbit
3
2
1
Optimal 1- departure orbit
Optimal without backups
2035 Opportunity
Departure opportunities from HEO occur for short durations near perigee passages

## Slide 18: LEO departure constraints
A transfer to the Moon is possible every 6–10 days for given RAAN
Transfers to HEO are available about once a month for a given RAAN (HEO nodal regression is slow)
Crew can launch to desired RAAN on any day due to Earth’s rotation

## Slide 19: Low-Earth Orbit Departures Single Impulse Mode
Declination < 51.6 deg before optimal TMI date increases DV
Dec. near -51.6 deg for several days. Optimal LEO stays in departure plane.
Min. DV for free choice of orbit on any day
DV as two different
orbits precess
2033, 51.6 deg inclination
2035, 28.5 deg inclination
Launch characteristics depend on launch declination

## Slide 20: 3-Burn with High-Earth Orbit
Min. DV for free inclination
Min. DV for 28.5 deg
free choice of RAAN
10-d HEO
(dashed)
4-d HEO
(solid)
Blue and green curves are different choice of LEO with different right ascension of the ascending node (RAAN)
10-d HEO has lower speed at apogee, which lowers reorientation DV
Three-burn sequence with intermediate HEO enables out-of-plane departures
2033, 28.5 deg inclination
2035, 28.5 deg inclination

## Slide 21: Departure Scenario Considerations for Human Missions to Mars
*
*For a 3–4 month cargo transfer, the DV reduces to 3100 m/s for L2 and to 3150 m/s for lunar orbit
*

## Slide 22: Example Mars Orbital Mission
600-day Mars mission with 60 days at Mars
Crew travels to Phobos (or any target orbit)
60-t Deep Space Vehicle
(NASA HEFT II Configuration)
10-t Space Exploration Vehicle
Storable Chemical Propulsion
Stage, 325 s Isp
DSV remains in loose orbit while crew travels to target orbit in SEV

## Slide 23: SEV Reduces Mass for Phobos Missions

## Slide 24: The Old Problem
Connect arrival and departure interplanetary trajectories via maneuver at apoapsis

## Slide 25: The Current Problem
Target orbit plane could be mismatched with interplanetary orbits
target orbit
target orbit

## Slide 26: Relative cost of orbit reorientation techniques
Change line of apsides
(argument of periapsis)
in orbit
Change line of apsides during arrival/departure maneuver
Rotate orbit along line of apsides
Mars orbit
250 km altitude periapsis
1 sol period
5 km/s V∞

## Slide 27: Transfer to Phobos
Maneuver sequence:
DSV capture into parking orbit from arrival traj.
DSV rotate from arrival to departure plane
SEV rotate to target plane and raise periapsis
SEV lower apoapsis to circular target orbit
SEV raise apoapsis to elliptical parking orbit
SEV rotate to departure plane and lower periapsis
DSV escape from parking orbit to departure traj.
Transfer
to Phobos
Phobos Orbit
Rotate along
line of apsides
Off-periapsis
arrival/departure
Apoapsis in plane with Phobos
1
2,3,6
4,5
7

## Slide 28: Same Mission, Different Transfers
Full DV weight on DSV
Equal DV weight on SEV and DSV
Arrival
Departure
Arrival
Departure
Retrograde
Parking Orbit
with
plane flip
at apoapsis
Direct
Parking Orbit
The optimal orbit orientation can change dramatically based on relative mass of the DSV and SEV

## Slide 29: Phobos/Deimos Proximity Orbits*
Phobos is a complex dynamical region with significant perturbations from Mars and the irregular shape of Phobos
We present orbit options first in an idealized force model and then propagate these orbits in a full-force model
Orbits at the L1/L2 Lagrange points are unstable and require control (i.e. station keeping maneuvers)
  The key questions for flying these orbits is how often a maneuver needs to be done and how quickly something goes wrong if a maneuver is missed
Distant Retrograde Orbits (DROs) are stable orbits that exist around secondary bodies (e.g. Moon, Phobos, Deimos).
    Most stable when they remain within in the plane of the target or are further from the target
    It is a relatively simple matter to transfer between DROs at different altitudes and also other orbits at the L1/L2 Lagrange points
*Proximity orbit analysis from Mark Wallace, Jeff Parker, and Dan Grebow

## Slide 30
Lyapunov Orbits
unstable
Halo Orbits
unstable
Vertical Orbits
unstable
“Distant” Retrograde Orbits
stable
Periodic Orbits in “Ideal” Model (Circular Restricted 3-Body Problem)
L1
L2
Phobos
To Mars
L1
L2
L1
L1
L2

## Slide 31
Phobos Instability and Orbit Period vs. Closest Approach Alt.
(Circular Restricted 3-Body Problem)
Highest Halo
Retrograde Orbits are Stable
Vertical and Lyapunov Orbits are the highest altitude “Lagrange” point orbits
longer period  more time for maneuvers
Note: Altitude is geodetic altitude relative to Phobos ellipsoid

## Slide 32: Flying an Unstable Orbit
Libration orbits (Halo, Vertical, etc) are unstable by nature
Navigating an unstable orbit:
  Accurate maneuvers (mm/s precision or better)
    Shouldn’t be too hard given large mass of spacecraft
    A bigger challenge will be to minimize “noise” DV
  Frequent station keeping maneuvers (SKMs)
    SKM every 2 hours preferred
    SKM every 3-4 hours tolerated
    Small maneuvers – on the order of mm/s
    Low fuel budget if maneuvers are performed frequently and accurately: ~ 1 m/s per month (est.)
  Frequent tracking and/or on-board navigation at Phobos
    We can collect navigation data using craters, limb observations, laser/radar ranging, or with navigation beacons
Orbits can be biased to escape (instead of impacting) when control is lost; orbits that escape should return to the vicinity of Phobos every 8 hours or so.

## Slide 33: Phobos L2 Halo orbit in Full-Force Model (with control)
L2
Viewed from above
Viewed from Mars (orbit is behind Phobos)
Viewed from the side
2 km minimum altitude
Phobos
Mars
Altitude shown relative to Phobos ellipsoid
L1 orbits are similar

## Slide 34: Phobos Vertical Orbit in Full-Force Model (with control)
L2
Viewed from above
Viewed from Mars (orbit is behind Phobos)
Viewed from the side
3.8 km minimum altitude
Mars
Phobos
Altitude shown relative to Phobos ellipsoid
L1 orbits are similar

## Slide 35: What happens if you stop station keeping? (Halo)
Viewed from above
To Phobos-trailing orbit
Departure
Impact

## Slide 36: Dual Orbit Strategy
Equatorial DROs used as a safe “parking spot” for the DSH (Deep Space Hab) spacecraft
DSH spacecraft temporarily moved to Vertical Orbit during landings to monitor EVA
  DSH spacecraft operated in “quiet mode” to maximize precision of orbit control
  Vertical Orbit can be biased so that if control fails, DSH will escape Phobos instead of impacting
  If DSH escapes, it can return in a few hours (because of Phobos’ short orbit period of 7.7 hours)
  Vertical orbit will keep the DSH close to the crew for abort scenarios and above the horizon for com link and video

## Slide 37
DROs
Δv versus DRO close approach altitude
It costs from 11-20 m/s to transfer from a DRO to a vertical orbit
To go from a DRO to the libration point (L1 or L2) costs roughly 11.5 m/s
Phobos DRO to Vertical Orbit Transfer (Circular Restricted 3-Body Problem)

## Slide 38: Mars Mission Trade Study
Chemical Propulsion for Crew (CP-Crew)
  300 kW SEP used to pre-place cargo at Deimos and High Earth Orbit (HEO)
  CP used for all trajectories with crew onboard
Solar Electric Propulsion for Crew (SEP-Crew)
    300 kW SEP used to pre-place cargo at Deimos and HEO
    CP used for Crew to HEO and Earth Departure
    700 kW SEP used for crewed interplanetary traj. to Mars
    CP used for exploration of Deimos and Phobos

## Slide 39: CP-Crew Mission
Earth
Deimos
Phobos
HEO
DSV assembled and moved to HEO
4. Each SEV can make two round-trips between Phobos and Deimos
DSH and SEVs left at Deimos
6. CM direct entry
Two SEVs and SCPSs pre-placed at Deimos
1. Crew uses SCPS to get to HEO
2. DSV uses CCPS to escape
3. CP traj to Mars, CCPS used for MOI
5. CCPS used for DSV maneuvers at Mars and Earth Return
2.5-2.6 year mission; 1-1.5 years exploring Phobos and Deimos

## Slide 40: CP-Crew Trajectory Example

## Slide 41: SEP-Crew Mission
Earth
Deimos
Phobos
HEO
DSV assembled and moved to HEO
Two SEVs and SCPSs pre-placed at Deimos
DSH and SEVs left at Deimos
4. Each SEV can make two round-trips between Phobos and Deimos
6. CM direct entry
1. Crew uses SCPS to get to HEO
2. DSV uses SCPS to escape
3. SEPS takes DSV to Mars and spirals to Deimos
5. SEPS used for Earth Return
7. SEPS returns DSV to HEO
2.7-2.8 year mission; 4-7 months exploring Phobos and Deimos

## Slide 42: SEP-Crew Trajectory Example

## Slide 43: IMLEO Comparison

## Slide 44: Thoughts on Refueling
Chemical Booster Refueling
  A chemical boost stage can be thought of as a propellant depot with engines.
  For many mission the boosters will have excess capability or unused abort propellant.
  If the boosters could transfer propellant between each other, this excess propellant could be accumulated and used on later missions.
SEP Stage Refueling
  SEP stages also carry 10% missed thrust margin that could be transferred from used stages to new ones.
  However, SEP stages have large arrays that are expensive, so there is also a potential benefit to having fuel tanks at a refueling waypoint to enable reuse of SEP stages.

## Slide 45: Modular SEP Stages
Eight 40 kW SEP Stages could provide an effective 320 kW Stage…
In this example configuration, the arrays would only shadow each other when the Sun was directly along the axis of the central cylinder, but if the spacecraft rotates 180 deg around the thrust vector, the shadows are removed

## Slide 46
The “Cosmic Butterfly” 1954,
Ernst Stuhlinger
“Each of the fifty-foot parabolic mirrors in the wings concentrates the Sun’s rays on a boiler at its focal point. Steam is developed, which drives a 200-kw turbo-generator in the base.”
“The current thus generated drives the main propulsions unit, an ion rocket in which powerful electric fields accelerate charged particles, shooting them from the rear of the rocket exactly as the electron gun in your TV set bombards the screen. Sunlight, then, is the power source, whereas cesium is the propellant.”
“Since its thrust is entirely inadequate to cope with the gravity of major planets, the Cosmic Butterfly never lands. It is assembled in space and shuttles between artificial satellites.”